## Slide 1
Rajeev Gandhi Memorial College of Engineering & Technology
Department of CSE (Artificial Intelligence & Machine Learning)
Smart Irrigation System
ML-Powered Automated Irrigation for Agriculture
Pathuru Guru Vishnu
23091A3317
Maddula Sumanth
23091A3351
Under the Guidance of: Mr. V. Phanishwara Hara Gopal M.Tech | Duration: 29/12/2025 – 08/04/2026 | A.Y. 2025-26

## Slide 2
Abstract
What is it?
An intelligent system that automates sprinkler irrigation for wheat crops using Machine Learning and Arduino embedded systems.
Key technologies:
Decision Tree ML Model
Arduino Uno microcontroller
DHT11, Soil Moisture & Rain sensors
Relay module + LCD display
Impact & Benefits
💧
Reduces water wastage
🌾
Improves crop productivity
🤖
Minimises manual intervention
🌧️
Auto-stops during rainfall
📊
Real-time LCD monitoring
♻️
Supports sustainable farming

## Slide 3
Problem Statement & Objectives
⚠ Problems with Traditional Irrigation
Over-irrigation → water waste & soil erosion
Under-irrigation → poor plant growth
Fixed schedules ignore real-time conditions
No integration of multi-sensor data
High labor cost for continuous monitoring
Rainfall not considered in irrigation logic
✅ Project Objectives
Monitor soil moisture, temperature, humidity & rainfall
Implement Decision Tree model for irrigation classification
Automatically control water pump via relay module
Stop irrigation immediately on rainfall detection
Reduce water wastage & improve efficiency
Display real-time data on 16×2 LCD screen

## Slide 4
System Architecture & Proposed Work
Sensors
Soil Moisture
DHT11 (Temp/Humidity)
Rain Sensor
Arduino Uno
Reads sensor values
Processes decision
logic in real-time
ML Decision
Tree Rules
if-else conditions
converted from
Decision Tree model
Relay Module
Controls water pump
ON / OFF signal
→
→
→
💧 Water Pump
Irrigation ON/OFF
based on soil moisture
and rain status
🖥 LCD Display
Shows temp, humidity,
soil moisture, rain
and irrigation status
🌱 Output Classes
0 = No Irrigation
1 = Moderate Irrigation
2 = High Irrigation
↓
↓
↓

## Slide 5
Machine Learning Model – Decision Tree
Why Decision Tree?
Simple, fast & easy to implement
Converts to if-else rules for Arduino
Uses Entropy & Information Gain
Handles multi-feature classification
Model Performance
88.6%
Accuracy
6,213
Dataset Size
80 / 20%
Training / Test
Decision Logic (Arduino Code)
if (rainfall == 1) {
return 0; // No Irrigation
}
if (moisture < 400) {
return 2; // High Irrigation
} else if (moisture < 700) {
return 1; // Moderate Irrig.
} else {
return 0; // No Irrigation
}

## Slide 6
System Requirements
🔧 Hardware
Component | Description
Arduino Uno | Main microcontroller
Soil Moisture Sensor | Measures soil water content
Rain Sensor | Detects rainfall
DHT11 Sensor | Temperature & humidity
Relay Module | Controls water pump
LCD Display (16×2) | Shows real-time status
Water Pump | Supplies water to field
💻 Software
Tool / Library | Purpose
Arduino IDE | Upload code to Arduino
Python | Build ML model
Pandas | Data preprocessing
NumPy | Numerical computation
Scikit-learn | Train Decision Tree
Proteus | Circuit simulation

## Slide 7
Results & Performance
88.6%
Model Accuracy
6,213
Dataset Rows
3
Irrigation Classes
4
Input Features
Chart: Test-set Prediction Distribution
| No Irrigation (0) | Moderate (1) | High (2)
Count | 697 | 458 | 88
Proteus Simulation
✅ Circuit validated before execution — all connections verified
✅ After execution, LCD showed sensor readings & irrigation level
✅ Relay toggled pump ON/OFF correctly based on decision logic
✅ Rain detection immediately stopped irrigation as designed
✅ System correctly classified: High / Moderate / No Irrigation

## Slide 8
Conclusion & Future Scope
✅ Conclusion
The Smart Irrigation System successfully automates irrigation using a Decision Tree ML model and Arduino.
Key achievements:
88.6% model accuracy on test data
Automatic pump control via relay module
Real-time LCD monitoring of all parameters
Reliable rain detection & irrigation halt
Cost-effective, low-complexity solution
🚀 Future Scope
🤖 Advanced ML algorithms for better accuracy
📡 IoT integration for remote mobile monitoring
☀️ Solar power for energy efficiency
🌡️ Additional sensors (pH, nutrients, light)
☁️ Cloud storage for historical data analysis
🌦️ Weather forecast integration for smarter planning
🌾 Multi-crop support with tailored irrigation profiles

## Slide 9
References
[1] S. Ghosh et al., Smart irrigation: A smart drip irrigation system using cloud, android and data mining, IEEE ICAECCT, 2016.
[2] S. Vaishali et al., Mobile integrated smart irrigation management using IoT, IEEE ICCSP, 2017.
[3] S. B. Saraf & D. H. Gawali, IoT based smart irrigation monitoring and controlling system, IEEE RTEICT, 2017.
[4] Goldstein et al., Applying machine learning on sensor data for irrigation recommendations, Precision Agriculture, 2017.
[5] Y. Chang et al., A machine learning based smart irrigation system with LoRa P2P networks, APNOMS, 2019.
[6] F. Capraro et al., Neural network-based irrigation control for precision agriculture, IEEE ICNSC, 2008.
[7] James, G. et al., An Introduction to Statistical Learning, Springer, 2013.
Thank You | Smart Irrigation System | Dept. of CSE (AI&ML), RGMCET